## Slide 1: Android controlled Remote Tennis Ball Collector
Team Members
Hasan Kumar Reddy A (09005065)
Bhanu Prakash V (09005050)
Vinod Reddy G (09005071)
Avinash Theetla (09005056)
CS308: ERTS Lab Group 14

## Slide 2: Problem Statement
Aim : To control the Fire Bird V motion using an android mobile
Utility : Tennis ball collection
Modes : Autonomous mode and Manual Mode
Notes :
  Image Processing using Open-CV on android mobile
  Remote Live Video Transmission via Wi-Fi Camera
  Mobile to Bot communication via Bluetooth

## Slide 3: Description
Our Fire Bird V functions as a tennis ball collector. It sends the video stream of environment in front of it via an IP Camera fixed in front of it. Android mobile downloads the video from the IP Address of camera and processes it for the presence of tennis ball. Then it sends appropriate signal to the bot via Bluetooth communication module.
Motivation
Setting up a PC is a cumbersome task, especially in times of emergency. Hence we switched to android mobile for image processing and sending the signals.

## Slide 4: Requirements Aimed
S.No. | Aim | Status
1. | Remote Video Transmission via Wi-Fi (Hardware) | completed
2 | Android Application (Software) | completed
3. | Image Processing on Android Mobile (Software) | completed
4. | Bluetooth signal Transmission (h/w + s/w) | completed
5. | Ball Picker (Arm) Construction | done
6. | Firebird application code | completed
7. | Completely wireless | done

## Slide 5: Project Plan
Weekly team-meet and work review - Not strictly followed.
S.No. | Milestone | Alloted to | Completed On
1. | Project Presentation | Vinod, Hasan | 7th March
2. | Identifying modules and allotment | All | 16th March
3. | Setting up the Wi-Fi Camera | Hasan | 29th March
4. | Received our order for Bluetooth module |  | 3rd April
5. | Android Application | Hasan | 7th April
6. | Image Processing Code | Vinod | 9th April
7. | Firebird Application Logic | Bhanu | 8th April
8. | Fixing Arm on Bot | Avinash | 9th April
9. | Bluetooth Transmission | Avinash, Hasan | 10th April
10. | Bluetooth Receiving | Bhanu, Vinod | 10th April
11. | Project Integration | All | 11th April

## Slide 6: Finite State Machine
Do Animation

## Slide 7: Tasks, Challenges & Innovation
Video Transmission
  Android doesn’t recognize the usual Ad-hoc network setup by PC
  Tried
    Rooting mobile, using various apps.
    Setting up a WLAN network bridge in PC - Worked
Android Application
  Loaded the video in a webview
    Default view from IP Camera shows four streams
    Ran Javascript on top of it to display just the video required.
  Initially loaded a snapshot and regularly updated it at fixed intervals
    Java timer made the app non-responsive sometimes

## Slide 8: Tasks, Challenges & Innovation
Open CV
  Installation on windows – a challenge by itself
    Tried many work arounds, online tutorials
    Finally could get it working – links in report
  Linking the OpenCV C++ code with Android Java
    Android jni – relatively simpler
  Usual approach using cvHoughCircles – slow
    Devised a new approach
      Pixel by pixel analysis

## Slide 9: Tasks, Challenges & Innovation
Hardware
  Camera mounting
    Front
      will block the sharp sensors
      will block grippers movement
    Top
      Gripper arp in its path
  Sensor
    Single sensor – missed the ball many times
  Solution
    Increase the arm’s length
    Place 2 sensors ON the Camera
    Fix the Camera in front of bot

## Slide 10: Tasks, Challenges & Innovation
Bluetooth Setup
  Identification & Procurement
    Help from Piyush, Lab Asst.
  Programming
Firebird Logic Implementation
  Identifying the correct sensor(s) reading under which the gripper arm should be signaled to pick the ball
  Understanding ( and fixing the gripper arm ) the behaviour of gripper arm for various values servo motor

## Slide 11: Assumptions & Limitations
Only orange colored objects in view are TT balls
Only one ball in the bots view
  Though our openCV code can distinguish and identify one of the balls, bot might get confused in few cases
Sensor value might change with hardware
Hardware
  Android :
    armv7 processor is recommended, because of have a floating point preprocessor (Open CV).
    Touch enabled – by design
    Bluetooth and Wi-Fi capability – most smart phones have it

## Slide 12: Test Criteria and Delays involved
Introduced a delay of 1s between any two consecutive communication.
  Android (Sony MT11i) takes about 0.5 – 1s to download, process and transmit the signal
  Share your PCs network with the WLAN setup,
    Otherwise, the download seemed to be very slow (20 s), apparently no reason which we could find
Once the ball is picked in auto mode, cannot pick any more balls until reset.
  By design
Drawbacks
  Android application seemed to crash when many other applications are running simultaneously.
    May be using more runtime memory
    Close all other applications before you start the app

## Slide 13: Re-usability
Have provided brief documentation and references to Open CV in android setup and usage
  Could save a lot of effort
  Also included the jni resources – cross compilation and linking
Modular nature
  Image Downloading
  Image Processing
  Communication
  Application
  codes are all separated via different classes.
In code documentation standards
  Followed the usual Java commenting style (eclipse friendly)

## Slide 14: Future Enhancement
Replace the Bluetooth communication with Wi-Fi sheild
  http://www.instructables.com/id/How-to-build-an-Arduino-WiFi-4x4-with-Android-Cont/
  http://asynclabs.com/store?page=shop.product_details&product_id=26&vmcchk=1
  Will make the whole application really remote
Use an existing or write an Open CV wrapper for android
  http://code.google.com/p/javacv/
Improve the UI control – use joystick
  Good project
    http://www.instructables.com/id/JabberBot-The-Arduino-robot-with-an-ATMega-brain-/